## Slide 1: CMSC 628 – Spring 2019 Introduction to Mobile Networks
Dr. Eyuphan Bulut
CMSC 628- Mobile Networks

## Slide 2: Mobile Communication World
Proliferation of mobile computing and communication devices starting late 90s
  Cell phones, laptops
  Handheld digital devices
  Personal Digital Assistants (PDA)
  Wearable computers
WiFi hot spots replaced wired access networks

## Slide 3: Infrastructure Networks
Devices on the network all communicate through an access point: a device that allows wireless devices to connect to a wired network using Wi-Fi
Challenges:
  it takes time and potentially high cost to set up the necessary infrastructure everywhere.
  Not works for dynamic environments
    E.g. rural or disaster areas

## Slide 4: Infrastructure-Less Networks
Decentralized type of wireless network
Self organizing or Infrastructure-less
It does not rely on
  preexisting infrastructure such as routers in wired networks
  access points in wireless networks
The wireless network nodes (e.g., the users’ mobile devices) communicate with each other to perform data transfer
Nearby users can communicate directly by exploiting the wireless technologies of their devices in ad hoc mode

## Slide 5: Mobile (Ad hoc) Networks (MANET)
Ad-hoc means ‘for this purpose’
  used to describe something that has been formed or used for a special and immediate purpose, without previous planning.
Self organizing networks (SON)
Wireless
transmission
range

## Slide 6: Mobile Ad hoc Network (MANET)
Each device is free to move independently in any direction, and will therefore change its links to other devices frequently
  Hence, it has a dynamic topology
The primary challenge in building a MANET is equipping each device to continuously maintain the information required to properly route traffic

## Slide 7: MANET forms
Single-hop
  Simplest form
  Direct connectivity
Multi-hop
  MANETs often refer to this form of connectivity

## Slide 8: Challenges
Infrastructure-less design adds difficulty in fault detection and management
Dynamic topology results in route changes and packet loss
Scalability is still unsolved, challenges include addressing, routing, configuration management, interoperability, etc.
Varied link/node capabilities cause variable processing capabilities
Energy constraints limit processing power; ad-hoc networks rely on each node being a “router”

## Slide 9: Applications of MANETs
Advantages: low-cost, flexibility
  Ease & Speed of deployment
  Decreased dependence on infrastructure
Applications
  Military environments
    soldiers, tanks, planes
  Civilian environments
    vehicle networks
    conferences / stadiums
    outside activities
  Emergency operations and disaster scenarios
    search-and-rescue / policing and fire fighting

## Slide 10: MANET History
In 2000-2005, MANET was one of the most innovative and challenging areas of wireless networking
  Numerous research efforts
Today, the promise of ad hoc networking never fully realized, and that MANET solutions are not used in people’s life
  A few practical deployments
    FireChat, Serval Project
  Reasons:
    Lack of real approaches/objectives in research
    Only theoretical parts of interesting research questions studied
    Mostly simulation based evaluation without real experiments

## Slide 11: MANET Research
Focus:
  Mostly focused on general purpose pure MANET
    No specific application
  Aimed to extend Internet services to non-infrastructure areas
  A complete redesign of network architecture and protocols
  Efficient communication algorithms
  Standardization efforts through IETF MANET Working Group
    IETF = Internet Engineering Task Force

## Slide 12: IETF MANET Working Group
https://datatracker.ietf.org/wg/manet/about/
“The purpose of the MANET working group is to standardize IP routing protocol functionality suitable for wireless routing applications within both static and dynamic topologies with increased dynamics due to node motion or other factors.”
“Approaches are intended to be relatively lightweight in nature, suitable for multiple hardware and wireless environments, and address scenarios where MANETs are deployed at the edges of an IP infrastructure."

## Slide 13: MANET Layers
MANET layered stack
Routing, forwarding
(most research here)
Modified TCP extensions
Research did not focus on here much
+ Cross-layer research issues

## Slide 14: MANET Networking Layer
Routing: identifying the path between a sender and a receiver
Forwarding: The subsequent function of delivering the packets on the routing path
Legacy wired network based routing problems do not work due to dynamic and unpredictable nature of MANET topology
MANET routing protocols have the following common features. They aim to
  discover a path from source to destination
  maintain that path (e.g., if an intermediate node moves and breaks the path)
  define mechanisms to exchange routing information

## Slide 15: MANET Casting
Routing protocols can be defined based on different casting approaches:
Unicast
Broadcast
Multicast
Geocast
Main stream routing algorithms use unicast

## Slide 16: MANET Routing Challenges
Routing overhead must be kept minimal
  Wireless  low bandwidth
  Mobile  low power
  Minimize # of routing control messages
  Minimize routing state at each node
Nodes must determine how to forward packets
  Source routing: Routing decision is made at the sender
  Hop-by-hop routing: Routing decision is made at each intermediate node
Difficult to achieve good performance
  Routes change over time due to node mobility
  Best to avoid long delays when first sending packets
  Best to reduce overhead of route discovery and maintenance
  Want to involve as many nodes as possible – to find better paths and reduce likelihood of partitions

## Slide 17: MANET Routing Protocols
Ad-Hoc Routing Protocol
Proactive Routing Protocol
Reactive Routing Protocol
Hybrid Routing Protocol
Hierarchical Protocol
Table-driven
Periodic distribution of routing tables among nodes
On-demand
Finds a route flooding Route Request (RREQ) packets
Combines the power of proactive and reactive routing
The choice of proactive and of reactive routing depends on the hierarchic level in which a node resides
Others: Energy-aware, Cluster-based

## Slide 18: Cross-Layer MANET Research
Some issues are not specific to a single layer:
  Energy efficiency
    Local and global strategies
    Should consider both individual node energy and its impacts to the network
      Always sleeping node without contributing to routing is not a good one
      Topology control (via sleep scheduling, controlling the transmission power) without compromising coverage is a good one
  Security
    Malicious nodes can disrupt the proper functioning of routing (e.g., false routing tables)
  Cooperation
    Incentives for collaboration, to avoid selfishness
    Virtual currency (paid for transmission, reward when forwarding others)

## Slide 19: Cross Layer Architecture
Interlayer Communications
  Additional communication channels between different layers
Interlayer Tuning
  Joint optimization of each independent layer
Interlayer Design
  Joint design of two (or more) layers.
Unlayered Design
MobileMAN* architecture
shared memory
*Borgia et. al.,MobileMAN: Design, integration, and experimentation of cross-layer mobile multihop ad hoc networks, IEEE Communications Magazine, 2006.

## Slide 20: Evolution of MANET
Why the MANET paradigm did not have a major impact? What are the lessons learned?
  Originally it was military research driven and could not make shift to civilian applications
    Limited off-the-shelf wireless network technologies
  Academia focused on interesting problems
  Scarce exploitation and low interest among the users
  Limited simulations and less credibility due to lack of implementation, integration and experimentation except a few (MobileMAN, Uppsala APE testbed, Darmouth College testbed)

## Slide 21: From MANET to…
What are the new technologies emerged from MANET?
  Mesh networks (integrated to infrastructure)
  Opportunistic networks
    Mobility as opportunity not a problem
  Application focused
    Wireless Sensor Networks (IoT Networks)
    Vehicular Networks

## Slide 22: Mesh Networks
Aims to reduce the MANET complexities with integration of fixed networks
Low-cost extension of Internet with a few hop wireless links
Research has focused on all of implementation, integration and experiments on real networks with real users
Traditional WLAN
Mesh Network

## Slide 23: Opportunistic Networks
Delay tolerant networks (DTN), Intermittently Connected Networks
Characteristics:
  No stable end-to-end path
  Store-carry-and-forward paradigm for routing
    Mobility not a problem but opportunity
Challenges:
  Online decision making
  Mobility understanding and modeling (e.g., inter-contact distribution)

## Slide 24: Vehicular Ad Hoc Networks (VANETs)
Motivated by Intelligent Transportation System (ITS) goals
  Reducing traffic congestions, road accidents..
Peculiar features of vehicular field
  Road structure, high speeds etc.
  New communication protocols: WAVE, DSRC
Inter-roadside communication
Inter-vehicle communication
Vehicle-to-roadside communication

## Slide 25: Wireless Sensor Networks (WSN)
Sensor and actuator networks (Cyber and physical components)
Data collection at sink, stable & mobile sensors, message ferries/robots
Extensive research done on:
  Topology control, energy saving, clock synch, coverage, connectivity, routing, MAC protocols
Limited unstudied topics:
  Security/trust, Quality of service, realistic simulations, underwater sensor networks
New extensions: Human-centric (mobile) sensing/computing, participatory sensing
Env. monitoring agent
Fire detection agent
Fire tracking agent

## Slide 26: WSN vs. IoT
WSN: a set of sensors that send their data to a sink, not necessarily connected to Internet
IoT: a set of (sensor) nodes that are connected to Internet (and cloud for analytics) either directly or via a gateway
Sink
Sensor node
Gateway
(Sensor) node
Cellular
Analytics

## Slide 27: What’s next?
Next class: Enabling Technologies for Mobile Networks
MANET:
  Medium Access Control (MAC)
  Routing Protocols
Opportunistic networks
  Routing algorithms, Mobility modeling, Analysis
Wireless Sensor Networks (IoT Networks)
Vehicular Networks